## Slide 1
Internal internship presentation
Soutenance – 05/07/2021
Maxime Georges
Misbehavior detection in CPM messages in a V2X network
Intership realised from march to july 2021
Internship tutors : Ines Ben Jemaa / Francesca Bassi

## Slide 2
Internship context
F2MD integration from Veins To Artery
Adding CPM features to F2MD
Overall features
Attacks
Checks
Results
Conclusion
Presentation overview
Notes: Ne pas parler de veins ni artery, juste des outils

## Slide 3
Presentation overview
Internship context
F2MD integration from Veins To Artery
Adding CPM features to F2MD
Overall features
Attacks
Checks
Results
Conclusion

## Slide 4
Internship context
SCA project
2017 - 2020
TAM project
2021 - 2024
F2MD Framework
Framework based on veins and omnet++, that implements:
A set of V2X attacks on CAM
Several CAM MbD algorithms
Visualize detections in real time
Generates dataset and reports sent to a Misbehavior Authority
My internship
Add CPM features to the F2MD framework, including:
A new set of attacks based on CPM
Several CPM MbD checks

## Slide 5
Presentation overview
Internship context
F2MD integration from Veins To Artery
Adding CPM features to F2MD
Overall features
Attacks
Checks
Results
Conclusion

## Slide 6
F2MD: from veins to Artery Limits of Veins
F2MD was built as an application module of Veins. Compared to other framework, Veins has several drawbacks:
Poor modularity: adding a new application module, of modify mobility services requires to modify backend code of veins
No sensors/perception module implemented. CPM implementation should be created from scratch
Do not take official regulation into account
Veins (car2x.org)
F2MD
Application layer
Data & report generation

## Slide 7
F2MD: from veins to Artery Advantages of Artery
Artery V2X Simulation Framework (v2x-research.eu)
Using Artery instead of veins offers several advantages:
Modularity of services, for each vehicles. Several services, including CAM, CPM and DEN are already implemented
Facilities already implemented offers useful functionalities, such as sensors
Artery was at first an extension of veins, so F2MD can easily be adapted for Artery

## Slide 8
locEnvMod
F2MD: from veins to Artery Local Environment Model
Each vehicles owns a local environment model, which is defined by :
An area, restricted by the type and the number of sensors located on the vehicle
All the vehicles that are located in this area are considered as “perceived” and thus are added in this environment model
Makes the CPM implementation easy

## Slide 9
F2MD: from veins to Artery Modularity of Artery
Sensors description
Let you assign different sensors to each vehicle of the simulation individually
Service description
Let you assign different services to each vehicle of the simulation individually
ASN regulation files
ASN regulation files
Describes the fields and the rules related to each types of V2X messages (CAM, CPM and DEN)
F2MD

## Slide 10
Main problems encountered
While porting F2MD to Artery
M
I
D
D
L
E
W
A
R
E
Facilities and others Artery back end code
Vanetza networking layers
Artery coords
Artery spatial system: heading and positions are differents
Vanetza packet type
Vanetza BSM fields
F2MD Veins App
Layer
F2MD
F2MD Files
Veins & INET layers
Veins coords
Veins spatial system: heading and positions are differents
INET packet type
INET mac address and BSM fields
Veins format
Artery format

## Slide 11
Main problems encountered
While porting F2MD to Artery
M
I
D
D
L
E
W
A
R
E
Facilities and others Artery back end code
Vanetza networking layers
Artery coords
Artery spatial system: heading and positions are differents
Vanetza packet type
Declaration of a new BSM type
F2MD Facility
F2MD
F2MD Files
Veins coords
Veins spatial system: heading and positions are differents
F2MD Service
Artery spatial system
Veins spatial system
conversion
getAttributes from facilities
(position, speed…)
Artery coordinates
Artery coordinates
Sends or reveices a new message
Veins coord

## Slide 12
Presentation overview
Internship context
F2MD integration from Veins To Artery
Adding CPM features to F2MD
Overall features
Attacks
Checks
Results
Conclusion

## Slide 13
Overal Architecture
Middleware
CAM Service
CPM Service
Service that allows vehicle to send (trigger) and receive (indicate) CAMs.
Service that allows vehicle to send (trigger) and receive (indicate) CPMs.
Triggers the sending of a CPM periodically
Indicates the reception of a new CPM

## Slide 14
CAM Parameters
Stores CAM related F2MD parameters
Overall Architecture
Middleware
CAM Service
CPM Service
Service that allows vehicle to send (trigger) and receive (indicate) CAMs.
Service that allows vehicle to send (trigger) and receive (indicate) CPMs.
Triggers the sending of a CPM periodically
Indicates the reception of a new CPM
CAM F2MD Processing
F2MD framework. Implements, among other features:
CAM attacks & checks
Pseudonyms
Report generation
CPM F2MD Processing
F2MD framework. Implements, among other features:
CPM attacks
CPM checks
CPM Parameters
Stores CPM related F2MD parameters

## Slide 15
Implemented attacks
CPM Data
Header
Sender ID
CPM ID
Management & vehicle data container
senderType
Ego GPS position
Ego speed
Ego heading
Perceived object container
For each perceived object:
Object ID
Time of Measurement
Distance Value & Conf.
Speed Value & Conf.
Yaw angle value & Conf.
18 Implemented attacks, based on :
Random Distance
Change the distance randomly
Random Speed
Change the speed randomly
Naïve attacks
Distance Offset
Adds an offset to the perceived distance
Speed Offset
Adds an offset to the perceived speed
Constant Offset
Adds an offset to all the perceived object attributes
Discrete attacks
Ghost Object
Adds a fake object to the list of percvd. objects
Drop Object
Remove a perceived object
Drop all Objects
Remove all the perceived objects
Malicious attacks

## Slide 16
Misbehaviour detection
Plausibility tests
Radar range
Distance Plausibility
Distance < MaxRadarRange
Speed Plausibility
Speed < MaxPlausibleSpeed

## Slide 17
Misbehaviour detection
Consistancy tests
Distance Consistancy
Speed Consistancy
Or

## Slide 18
Misbehaviour detection
Predictive tests
Distance Prediction
Let’s define :

## Slide 19
Main problems encountered
While creating CPM features
Cpm is already implemented in Vanetza/Artery, following the ETSI regulation
Thus, each cpm sent must fulfil all the requirements defined in this regulation
Measurements units
Positions, speeds and heading – among other CPM-fields – must be declared in the correct units (centimetres, degrees…). If not, the CPM is not sent.
Pseudonym redundancy
senderID can only take a value between 0 and 255. In huge scenarios, this can cause several vehicles to have the same ID. Worse, we currently use the two last digits of the artery ID of each vehicles which sometimes cause ID repetitions even with a 10 vehicles scenario
Tests and logging must be adapted
Debbugging or logging values cannot be sent through the CPM, as it is not defined in the regulation

## Slide 20
Scenarios
Highway test Scenario
Simple highway scenario useful for testing
Unlimited amount of cars and scenario time
2 ways highway ( vehicle can cross each others
Vehicles can overpass if their speed is different
Vehicles are the same during all the simulation
Highway
IRTS complex Scenario
Complex scenario with a city-like environment
Unlimited amount of cars and scenario time
Multiple intersections and buildings
Vehicles can exit and enter the map at any time
User can choose between CAM, CPM, and both
IRTS

## Slide 21
Examples
Example 1
Scenario Highway
5 vehicles
2 attackers
Penetration rate 100%
Attack: Offset Random
Result: all attackers are detected with basic tests

## Slide 22
Examples
Example 2
Scenario Highway
15 vehicles
4 attackers
Penetration rate 100%
Attack: Offset Random
Result: all attackers are detected with basic tests, apart from one that does not perceive any objects

## Slide 23
Examples
Example 3
Scenario Highway
5 vehicles
2 attackers
Penetration rate 100%
Attack: Ghost Objects
Result: Basic tests does not allow to detect such attacks. One attackers is detected because of redundant pseudonym

## Slide 24
Random Sped
Change the speed randomly
Offset attack / 5 vehicles
Results
40% of attackers ( id {97; 76} ) – 100% penetration rate
Random distance offset
30 seconds – 1 CPM / second
True positive
True Negative
False Negative

## Slide 25
Next steps
End of the internship
Start of the thesis
Solve minor problems
Pseudonyms redundancy, tests fail or innacurate
Write a documentation
So that this code can be used and modified with ease
Add all missing features to CPM F2MD
There is still a lack of features in CPM facility compared to CAM
Test the complete Framework in various complex scenarios
The framework must be robust and efficient on highly complex scenarios, such as IRTS

## Slide 26
Presentation overview
Internship context
F2MD port from Veins To Artery
Adding CPM features to F2MD
Overall features
Attacks
Checks
Results
Conclusion

## Slide 27
Thank you for listening
Please feel free to ask questions